## Slide 1: PROBA2 a Space Weather Monitor
Matthew J West
ESWW10 - Nov 2013

## Slide 2
Microsatellite in sun-synchronous orbit
Launched on November 2, 2009
725 km altitude ☀ Period: ≈100 min
Commanding and data processing at P2SC (ROB, Brussels).
Funded by ESA / SSA
PROBA2
Movie: ESA

## Slide 3
PROBA2 originally an ESA technology mission.
Currently a scientific instrument and space weather tool.
PROBA2 - 4 innovative instruments
Large Yield Radiometer (LYRA)
Sun Watcher using APS & Image Processing (SWAP, an EUV imager)
Two instruments to monitor solar activity – operated from P2SC Belgium
The Dual segmented Langmuir probe (DSLP)
Thermal Plasma Measurement Unit (TPMU)
Two particle detectors to monitor the plasma environment of the spacecraft.

## Slide 4
Exercise in miniaturization: off-axis Ritchey-Chrétien scheme.
Observes the 1 million degree corona in EUV light
SWAP – EUV Imager

## Slide 5
LYRA – Large Yield Radiometer
LYRA monitors the solar irradiance in four UV pass-bands.
Chosen for their relevance to solar physics, aeronomy and Space Weather:
Lyman-α channel (120-123 nm)
Herzberg continuum channel (190-222 nm )
Aluminium filter channel (17-80 nm + a contribution below 5 nm), including strong He II at 30.4 nm
Zirconium filter channel (6-20 nm + a contribution below 2 nm), rejecting He II.
Providing time series of solar irradiance with a very high sampling cadence (up to 100 Hz).
The wavelengths are complimentary to GOES/EUVS, SDO/EVE, SOHO/SEM etc.

## Slide 6
PROBA2 as a Space Weather Monitor
&
Observing the sources of Space Weather

## Slide 7
Observing Flares I
13th Jun 2012, at 11:29 UT, an M1.2 flare occurred in AR11504
Useful for observing the sources of space weather.
LYRA
SWAP

## Slide 8
Limited blooming due to CMOS detector
Nominal cadence of ~2 min
Max cadence ~18 sec
2010 02 07 00:14:00
EUVI-A
02:40
2010 02 07 00:14:15
02:44
Observing Flares II – SWAP Limited Blooming

## Slide 9
Nominal temporal resolution of 20 Hz
Maximum temporal resolution of 100 Hz
M-flare 20 Jan 10
Observing Flares III – LYRA High Resolution
Notes: Fig 4 shows LYRA channels 1, 3, and 4 normalized between their min and max, plus the first derivative of channel 3 in arbitrary units on the 0.25 level. You see here a subset containing 15 minutes of the flare. It is obvious that the Lyman-alpha curve precedes the short-wavelength channels and somehow follows the derivative. - I leave it to the specialists to explain what the derivative of the SXR has to do with the HXR and with Lyman-alpha or Bremsstrahlung. Absolutely not my field.
Al = 0-4 nm & 17-60 nm
Zr = 0-3 nm & 7-20 nm
There are two types of flares: Flares which rise very quickly, and flares
that rise slower. The impulsive ones have a correlating signal in the
Ly-alpha channel, even when they are not so strong.
possible candidates are flare numbers:
5800 (M1.8)
6880 (C9.9)
7080 (C4.2) incl. its unclassified follower
7510 (C6.8)
7790 (M1.0)
As mentioned before, a certain strength is necessary, but it is not the only condition: there must be a very fast rising phase.
Page 2 shows a 1-hour subset of these three hours, between 13:30 and 14:30 UTC. According to GOES, this flare starts at 13:32 (which I cannot confirm), has its peak at 13:47, and "ends" (half-max?) at 13:50. This figure is shown in the full data resolution: gaps are filled relative to page 1, and the widths of the curves show the noise variation. It becomes obvious that the flare as shown in the short-wavelength channels is not smooth but has a structure, and that the flare consists of several parts (e.g. varying velocities in the rising phase). On the other hand, it does *not* contain a spacecraft rotation nor an eclipse, which helps a lot.

## Slide 10
Solar Activity
We can observe various forms of solar activity:
Flares
CMEs
Prominence eruptions
EIT Waves

## Slide 11
Active Regions (Inverted colours)
Notes: Inverted color table

## Slide 12
Discussion I
PROBA2 is an effective Space Weather monitor.
Provides:
High cadence, Large view, EUV imaging (SWAP)
Prominence eruptions / CMEs
EUV Jets
Flares
ARs
High cadence Solar irradiance observations (LYRA)
Flares
Eruptions

## Slide 13
Discussion II
Advantages of a small mission:
We can easily undertake special off pointing campaigns.
Useful for prominence, CME and comet tracking.
We can control the satellite from anywhere with an internet connection.

## Slide 14
Discussion III
PROBA2 has two downlink stations:
REDU (Belgium) & Svalbard.
We receive data every 2-3 hours.
Once the data reaches the ground -> ~30 minutes to prep and output.
However, due to the low altitude polar sun sync orbit:
We have eclipse seasons which interrupt signals and potentially miss events.
Experience interference from SAA
Note, we attempt to use both events to study the atmosphere.

## Slide 15: www. http://proba2.oma.be/

## Slide 16
For more information and to discuss the potential of PROBA2:
Visit the PROBA2 stand at the ESWW Fair on Wednesday 16:30
The PROBA2 Splinter Session on Thursday 17:15-18:45